## Slide 1
MARKETCAR CONNECT
Self‑Hosted WebRTC
Across a Routed Network
MiroTalk P2P • Proxmox • Docker • Containerlab
Network Programming Project
Prepared by Izz Aldeen Mansour
An‑Najah National University

## Slide 2
NETWORK PROGRAMMING PROJECT
The goal was bigger than running a video app
02
Izz Aldeen Mansour
The course required a real service,
inside a real network path.
Success meant proving the complete chain — not only opening a webpage.
01
Deploy
Host a real-time application on a server
02
Route
Reach it from isolated client networks
03
Integrate
Consume the service from another application
APPLICATION
NETWORK
SERVICE INTEGRATION

## Slide 3
NETWORK PROGRAMMING PROJECT
We evolved the project in five validated stages
03
Izz Aldeen Mansour
1
LocalConnect
Node.js + Socket.IO
proof of concept
2
MiroTalk P2P
Real WebRTC rooms
and media features
3
Proxmox
24/7-style Ubuntu
server environment
4
Containerlab
Two routed client
networks
5
MarketCar
Consumer app launches
meeting rooms
Each stage reduced risk before the next layer was added.

## Slide 4
NETWORK PROGRAMMING PROJECT
The final design separates consumer, service, and network
04
Izz Aldeen Mansour
MarketCar
Consumer application
port 5001
MiroTalk P2P
Self-hosted WebRTC service
port 3000
Buyer + Seller
Video • audio • chat
screen sharing
room URL
real-time media
INFRASTRUCTURE FOUNDATION
Proxmox → Ubuntu pserv → Docker Compose
NETWORK VALIDATION
Containerlab routed clients
HTTPS

## Slide 5
NETWORK PROGRAMMING PROJECT
MiroTalk P2P was the balanced technical choice
05
Izz Aldeen Mansour
C2C
One-to-one
Simple deployment
Limited project scope
P2P
Meeting rooms
Video + audio + chat
Screen sharing
Strong course fit
SELECTED
SFU
Large conferences
Higher scalability
Heavier architecture
Enough capability for a convincing demo — without SFU complexity.

## Slide 6
NETWORK PROGRAMMING PROJECT
The service runs on a dedicated virtualized stack
06
Izz Aldeen Mansour
HP physical server
Standalone university-lab device
Proxmox VE
Virtualization and lifecycle control
Ubuntu VM — pserv
Server IP: 172.16.107.5
Docker Compose
Repeatable service deployment
MiroTalk P2P
Listening on port 3000
Operational proof
Health
HTTP/1.1 200 OK
Runtime
Docker container: mirotalk
Control
docker compose up -d
HTTPS
Nginx self-signed local access
curl -I http://127.0.0.1:3000

## Slide 7
NETWORK PROGRAMMING PROJECT
The routed lab connects two client networks to the service
07
Izz Aldeen Mansour
Client 1
10.10.1.10/24
Router 1
10.10.1.1/24
10.10.12.1/30
Router 2
10.10.12.2/30
10.10.2.1/24
Client 2
10.10.2.10/24
Ubuntu host / pserv
miro-srv: 10.30.0.10/24
MiroTalk :3000
10.10.1.0/24
10.10.12.0/30
10.10.2.0/24
10.30.0.0/24
Static host routes return traffic to both client subnets through 10.30.0.1.
Current router image: Nokia SR Linux on R1 and R2

## Slide 8
NETWORK PROGRAMMING PROJECT
Reachability was verified at both network and service levels
08
Izz Aldeen Mansour
$ sudo containerlab inspect --all
$ docker ps --format "table {{.Names}}\t{{.Status}}"
$ sudo ./scripts/test-lab.sh
$ wget -S -O /dev/null http://10.30.0.10:3000
HTTP/1.1 200 OK
$ ip addr $ ip route $ traceroute -n 10.30.0.10
What the evidence proves
Nodes
All lab containers are running
Routes
Clients have a valid path to pserv
Service
Port 3000 returns HTTP 200
Media
Browsers can open the meeting room
HTTP success is stronger than ping alone: it proves the application responds.

## Slide 9
NETWORK PROGRAMMING PROJECT
MarketCar turns communication into a reusable service
09
Izz Aldeen Mansour
تواصل مع البائع عبر الفيديو
One configuration point
const MIROTALK_BASE_URL = "https://…";
1
Select a vehicle
2
Enter the buyer name
3
Generate a unique room ID
4
Open MiroTalk in a new tab
/join/car-id + buyer + unique-code

## Slide 10
NETWORK PROGRAMMING PROJECT
Temporary HTTPS tunnels enabled secure access
10
Izz Aldeen Mansour
MarketCar
Local server :5001
VS Code Public Dev Tunnel
Cloudflare HTTPS
Quick Tunnel over HTTP/2
temporary public URL
MiroTalk
pserv :3000
secure media permissions
browser access
encrypted tunnel
Why this path?
HTTPS is required for reliable camera and microphone access outside localhost.
University Fortinet blocked ngrok and Tailscale certificate flows.
Trade-off: the Quick Tunnel URL changes after restart; only one variable must be updated.

## Slide 11
NETWORK PROGRAMMING PROJECT
The live demo follows one short, evidence-first sequence
11
Izz Aldeen Mansour
01
Service
docker compose up -d
curl -I 127.0.0.1:3000
02
Topology
sudo containerlab inspect --all
docker ps
03
Reachability
./scripts/test-lab.sh
wget … 10.30.0.10:3000
04
Integration
Start Cloudflare tunnel
MarketCar → video meeting
End with two devices inside the same MiroTalk room: video, audio, chat, and screen share.

## Slide 12
THE RESULT
A complete service path —
from network to user experience.
Self-hosted
MiroTalk on pserv
Routed
Two client subnets
Verified
HTTP 200 from clients
Secure
HTTPS tunnel for media
Integrated
MarketCar launches rooms
Next: multi-vendor router image • persistent domain/tunnel • TURN for restrictive NAT
The project now demonstrates application, infrastructure, routing, secure access, and integration.
Questions & live demo